## Slide 1
MPPT
CHARGE
CONTROLLER
GROUP-13

## Slide 2
Role of a Charge Controller?
Ensure Safety of Battery
  Over Charging
  Deep Discharging
  Proper charging parameters
Ensure safety of Solar Panels
  Dusk/ night : Back flow protection
Effective power management
Direct Connection
PWM Charge Controller
MPPT

## Slide 3: WHY MPPT?
But due to environmental fluctuations
MPPT Algorithm must constantly tracking the Maximum power point. It increases the efficiency by 30%

## Slide 4: IMPLEMENTATION OF MPPT
Several methods exists.
  Perturb and Observe method
  Incremental conductance method
  Constant voltage method
Perturb and Observe method(Our Project uses this method)
Easy to implement
constantly checking the voltage (or current in some systems) and continuing to increase the voltage as long as the power continues to increase
Disadvantage is the system oscillates around the power point
Incremental Conductance Method
Implementation is complex
Accuracy is higher than P & O method

## Slide 5: MPPT ALGORITHM(P & O Method)
•Simplest method of MPPT
•Hill climbing method on two-point power comparison method
Concept

## Slide 6: Flow Chart

## Slide 7: Functional Block Diagram

## Slide 8: Specifications
40V, 30A Input(Solar, Wind Turbines, PSU)
  12V OUTPUT/ BATTERY - 420W @35A
  24V OUTPUT/ BATTERY - 840W @35A
Wi-Fi & Bluetooth
98% Peak conversion efficiency
Battery & Input Disconnect Recovery Protocol
Settable PWM Switching Frequency(1.2kHz - 312kHz)

## Slide 9: What to Expect ??
30V,10A Input(Solar)
  12V OUTPUT/BATTERY - 60W@5A
90 % Peak-Conversion Efficiency
Settable PWM Frequency
Two 12V Smart lighting system as Load (20W)

## Slide 10: Buck Converter

## Slide 11: Asynchronous Buck Converter
Typical Efficiency: 75-87%
Notable power loss across the diode’s forward voltage drop
Easy and straight forward implementation
Solution : Synchronous Buck Converter

## Slide 12: Synchronous Buck Converter
Typical Efficiency: 88-98%
Minuscule losses formed across MOSFET’s on-resistance
Proper implementation of switching required.
Solution : Use Half-Bridge MOSFET driver

## Slide 13: Half-Bridge MOSFET driver (IR2104)
Fully operational to +600V.
Gate drive supply range from 10 to 20V.
High side output in phase with input.
Shut down input turns off both channels

## Slide 14: MOSFET Selection
Should be capable of high frequency switching.
Should be capable of high drain current.
Should have low on-resistance.
Low conduction loss and switching loss.
We have chosen IRFZ48N MOSFET.

## Slide 15: Inductor Selection
We are design solar panel.
Input voltage
Output voltage
Ripple current is taken as of
PWM frequency
We plan to wind a toroidal inductor with
Reference : Texas Instruments

## Slide 16: Output Capacitor Selection
Output capacitance is required to minimize the voltage overshoot and ripple at the output.
Should have low equivalent-series resistance (ESR).
Output ripple voltage is taken as
Required output capacitor.
Reference : Texas Instruments

## Slide 17
Voltage Measurement
Two voltage divider circuits are used to measure solar panel and battery voltage.
Two analog pins of the esp32 are used to read voltages.
Vout = R2/(R1+R2) x Vin
Vin = (R1+R2)/R2 x Vout
Solar Panel = ADC x 0.0049 x (R1+R2)/R2
For the battery voltage measuring
For the solar panel voltage measuring
Voltage
Count

## Slide 18
Current Measurement
ASC712 (5A) current sensor is used to measure the current.
ASC712 current sensor :
Value = (5/1024) x analog read value
Sensitivity is 185mV/A
The sensor can measure positive and negative currents (-5A to +5A)
The power supply is 5V
Offset is 2.5V
Current in amp = (value-2.5)/0.185

## Slide 19
Battery Charging Stages
Click to add text

## Slide 20: DRIVING LOAD...!
No Requirements for Faster Switching
Protection : Fuse and TVS Diode

## Slide 21: Power Supplies
LINEAR REGULATOR
V_out = V_ref (1+R1/R2)
V_ref = 1.25V
Dc-Dc Buck Converter

## Slide 22
SAFE OPERATION....!

## Slide 23
BODY DIODE CURRENT LEAKAGE
SCHOTTKY DIODE
MOSFET & MOSFET DRIVER
ISOLATED POWER SUPPLY
REVERSE BLOCKING MOSFET CONFIGURATION
NEED FOR A BETTER DESIGN ?

## Slide 24: IMPLEMENTATION LEVEL
LIGHTENING OVER VOLTAGE SURGE : TVS DIODE
AUTO LOAD DISCONNECTION : DEEP DISCHRAGING
ENSURING PROPER CHARGING PARAMETERS
  SWITCHING TO CONSTANT VOLTAGE STAGE
  BATTERY TEMPERATURE
PROTECTION AGAINST FAILURES

## Slide 25: PLACES WHERE WE EXPECT PROBLMS
DUTY CYCLE OF PWN SIGNAL : LOWER SIDE MOSFET
NON-LINEAR RESPONSE OF ADC (ESP32)
  External Precision ADC : AD1015 (12-bit resolution with 3800sps speed)
  HIGHER -> Finer Voltage and Current Steps , Power Handling
PWM FREQUENCY SELECTION :
LOWER -> Switching losses are low
ESP32 : 16 PWM PINS
16 bit resolution : 1.22kHz
12 bit resolution : 19.5kHz
11 bit resolution : 39.06kHz
10 bit resolution : 78.12kHz

## Slide 26: Trying to do better...!
LARGER STEP :
OSCILLATION
SMALLER STEP :
FASTER CHANGING CONDITIONS
ADAPTIVE STEP SIZE

## Slide 27
SOLUTION : 5-STATE MODEL
PARTIAL SHADING
BURST CHARGING

## Slide 28: EXCITED TO EXPERIMENT...!